## Slide 1: Lab 01: Introduction to Vivado & Logic Gates
Presented By: (Name)

## Slide 2: Chips, what? An IEEE CEDA Education Initiative
Presenter name

## Slide 3: Lab 01 Part 0: Vivado

## Slide 4: Vivado

## Slide 5: Vivado
AMD XILINX Vivado 2024.2:
Synthesis & analysis of HDLs
Block design integration
Included logic simulator
GUI-based commands
Each laboratory session is prepared as a stand-alone project

## Slide 6: Start a Laboratory Session
Start a new laboratory session with Vivado:
To each laboratory session corresponds a Vivado project directory:
  Lab01
  Lab02{a,b,c}
  Lab03{a,b,b_synth,c,c_synh,_soc}
  Lab04
Inside each Lab directory, there is the project for the current laboratory

## Slide 7: Inside a Project Folder
A project is made of different files carrying different information regarding the project:
srcs (sources): the descriptions of the components of the blocks of the projects.
sim (simulation): the file useful to the EDA tool to simulate the project.
Other files: generated by the tool to run the project and generate the implementation.
The Project File
To open a project, double-click on the Project File

## Slide 8: Vivado a First Glance

## Slide 9: Vivado a First Glance
Flow Navigator, to navigate inside the project, it is possible to change the view, from simulation, through synthesis to implementation

## Slide 10: Vivado a First Glance
Sources, contain the handwritten description of the modules used during the current laboratory

## Slide 11: Vivado a First Glance
The information panel, contains information regarding synthesis, implementation, errors, warnings and info

## Slide 12: Vivado a First Glance
The main window of the project, contains the project summary, the block diagram of the design and other useful windows

## Slide 13: Lab 01 Part 1: Create the First Gate

## Slide 14: Create a Block Design
A Block Design is a canvas to place structural components for our design:
Create a new block design:
  PROJECT MANAGER →
  IP INTEGRATOR → Create Block Design
“Create Block Design” window will appear:
“Design name”: xor_bd
“OK”
1.
2.
3.

## Slide 15: Modules in a Block Design
Modules are “ready to place” components in the design. They can be simple logic gates or complex digital circuits:
Right-click on the main window
Select Add Modules…
A new window with the available modules will pop up
2.

## Slide 16: Modules in a Block Design
Module version
Module name

## Slide 17: Instantiate a Module
Modules are “ready to place” components in the design. They can be simple logic gates or complex digital circuits:
Right-click on the main window
Select Add Modules…
A new window with the available modules will pop up
2.

## Slide 18: Input & Output Ports
Ports are the connections of our circuit with the external world, they provide the input and show the output:
Right-click on the main window
Select Create Port…
A new window with the ports settings will pop up
2.

## Slide 19: Input & Output Ports
It is important to name appropriately the ports (_i for inputs and _o for outputs), so the EDA tool can understand how to map them to the die:
Input (Direction: Input, Type: Other):
A_i, B_i
Output (Direction: Output, Type: Other):
Y_o
Input
Output

## Slide 20: Input & Output Ports
It is important to name appropriately the ports (_i for inputs and _o for outputs), so the EDA tool can understand how to map them to the die:
Input (Direction: Input, Type: Other):
A_i, B_i
Output (Direction: Output, Type: Other):
Y_o
Input
Output

## Slide 21: Interconnections
Connect the different logic gates to create the circuit:
  With the mouse over on an input, click and drag to another connection point
  Connect all the logic gates and the ports
Validate the design
1
↓
2 →

## Slide 22: Generate the Design
The EDA tool generates the code of our design taking into consideration the input and output ports of the chip:
Right-click on block design “xor_bd” in Design Sources
Select Create HDL Wrapper…
A new window with the available modules will pop up
Ok
1.
2.

## Slide 23: An In Deep Look to the Generated Design
`timescale 1 ps / 1 ps
module xor_gate (
A_i,
B_i,
Y_o );
input A_i;
input B_i;
output Y_o;
assign y = a ^ b;
endmodule

## Slide 24: Verify the Design
After the Block Design is complete, it is important to check the functionalities of our design with a simulation:
Left-click on Run Simulation in the Flow Navigator window
Run Behavioral Simulation
A new panel with the behavior of our design will appear, from there we can check its functionalities

## Slide 25: Lab 01 Part 2: Logic Gates

## Slide 26: Evaluate the Logic Gates
We have seen how to create a project and how to implement a XOR logic gate.
Now try to implement others Boolean Functions and evaluates their outputs.
and_bd
Evaluate the AND Gate

## Slide 27: Evaluate the Logic Gates
We have seen how to create a project and how to implement a XOR and AND logic gates.
Now try to implement others Boolean Functions and evaluates their outputs.
not_bd
Evaluate the NOT Gate

## Slide 28: Evaluate the Logic Gates
We have seen how to create a project and how to implement a XOR, AND, and NOT logic gate.
Now try to implement others Boolean Functions and evaluates their outputs.
or_bd
Evaluate the
OR Gate

## Slide 29: Lab 01 Part 3: The Multiplexer

## Slide 30: Combining Logic Gates
To create complex logic functions designers combine basic logic gates together.
The multiplexer is a digital circuit that choose an input among different with a control signal.

## Slide 31: Combining Digital Blocks
As logic gates digital blocks can also be combined to form more complex structures

## Slide 32: Practice Time
…again

## Slide 33: Test All the Logic Gates
The modules available for the laboratory also include other common logic gates.
Connect all the logic gates to a multiplexer and test them directly on the board.

## Slide 34: Lab 01 Part 4: Implementation

## Slide 35: Implement the Circuit on the Board
Click on “Generate Bitstream” and the EDA Tool will provide the files to upload the design on the board
Open the “Hardware manager”

## Slide 36: The Hardware manager
The Hardware Manager handles the connections with the board.
To connect:
  Open target
  Auto Connect

## Slide 37: The Hardware manager
To program the device, click on Program device, then Program
Now your design is working on the board!

## Slide 38: Authorship & License
These slides are distributed under the Creative Commons license "Attribution – Non-commercial - Share alike 2.5 Italy (CC BY-NC-SA 2.5)"
You are free to:
  to reproduce, distribute, communicate to the public, exhibit in public, represent, perform and recite this work
  to modify this work
Under the following conditions:
  Attribution - You must attribute authorship of the work to the original authors and in a way that does not suggest that they endorse you or the way you use the work.
  Non-commercial - You may not use this work for commercial purposes.
  Share Alike - If you alter or transform this work, or if you use it to create another, you may distribute the resulting work only under an identical or equivalent license to this one.
http://creativecommons.org/licenses/by-nc-sa/2.5/
Christian Conti christian.conti@polito.it
Gianvito Urgese gianvito.urgese@polito.it
Daniele Jahier Pagliari daniele.jahier@polito.it
Enrico Macii enrico.macii@polito.it
Cristiana Bolchini cristiana.bolchini@polimi.it
Fabrizio Ferrandi fabrizio.ferrandi@polimi.it
License
Authors