## Slide 1: Lab 02: Design of an Adder
Presented By: (Name)

## Slide 2: Electronic Design Automation Tools
Electronic Design Automation (EDA) are a suite of software, hardware, and services to assist in:
    Design;
    Implementation;
    Verification;
    Manufacturing;
EDA tools help engineers and designers automate complex tasks in the creation of electronic hardware.

## Slide 3: Hands-on: An Adder
We have seen how an EDA tool can help explore the design space of a project.
It is time to deploy a real circuit from its specifications to its implementation.
We will focus on a circuit that performs a simple mathematical operation: The addition (of bits)

## Slide 4: Lab 02 Part 1: Half Adder

## Slide 5: Summing Two Bits
How do we sum two bits?
Simple rules, similar to “standard” (decimal) arithmetic:
  0 + 0 = 0
  0 + 1 = 1
  1 + 0 = 1
  1 + 1 = ?

## Slide 6: Summing Two Bits
What about 1+1?
  With one bit, I can only represent 0 and 1… No “2” available.
  Similar to 9 + 1 in decimal… How do you express the result?
   Add one more “digit”. In our case, one more bit
  1 + 1 = 10
10 in binary = 2 in decimal

## Slide 8: A (first) Truth Table for Bit-Addition
 |  | SUM (C) on two bits | 
A | B | C1 | C0
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
Truth table with more than one output… this is new!
  How do we proceed?

## Slide 9: A (first) Truth Table for Bit-Addition
A | B | C1
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | B | C0
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Simply split it in two tables and treat them separately

## Slide 10: A (first) Truth Table for Bit-Addition
A | B | C1
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | B | C0
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Have we seen this function already??

## Slide 11: A (first) Truth Table for Bit-Addition
A | B | C1
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | B | C0
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 12: A (first) Truth Table for Bit-Addition
A | B | C0
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A | B | C1
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
And this one??

## Slide 13: A (first) Truth Table for Bit-Addition
A | B | C1
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | B | C0
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 14: A (first) Circuit for Bit-Addition
First circuit to implement 1 bit + 1 bit addition.
Called a HALF ADDER

## Slide 15
Let’s get our hands dirty….

## Slide 16: RTL Design of an Adder
Open the Vivado project for the Lab02 and create a new block design:
  IP INTEGRATOR → Create Block Design, on the left Flow Navigator bar
The “Create Block Design” window will appear:
  “Design name”: half_adder
“OK”
1.
2.
3.

## Slide 17: RTL Design of an Adder
Our project has been created, now we can implement the architecture of the adder:
  Add to the design the input ports
  Add to the design the output ports
  Add the logic gates of the half adder and connect the circuit to the input and output ports
  Simulate the circuit to verify its correctness
Look at the example seen in LAB1, and try to do the same steps for the Half Adder circuit…

## Slide 18: RTL Design: Input & Output Ports
Add the input and output ports:
  Right-Click → Create Port…
  Input (Direction: Input):
    A, and B are the input ports
  Output (Direction: Output):
    C0 and C1 are the output ports
Input
Output

## Slide 19: RTL Design: Input & Output Ports
Add the input and output ports:
  Right-Click → Create Port…
  Input (Direction: Input):
    A, and B are the input ports
  Output (Direction: Output):
    C0 and C1 are the output ports
Input
Output

## Slide 20: RTL Design: Logic Gates
Add the logic gates to build our full adder:
  Right-click → Add Module…
  From the list choose the correct gates
  OK
A & B →

## Slide 21: RTL Design: Logic Gates
Add the logic gates to build our full adder:

## Slide 22: RTL Design: Interconnections
Connect the different logic gates to create the circuit:
  With the mouse over on an input, click and drag to another connection point
  Connect all the logic gates and the ports
Validate the design
1
↓
2
↓

## Slide 23: Generate the Design
The EDA tool generates the code of our design taking into consideration the input and output ports of the chip:
Right-click on block design “half_adder” in Design Sources
Select Create HDL Wrapper…
A new window with the available modules will pop up
Ok
1.
2.

## Slide 24: Verify the Design (Simulation)
Simulate the design and verify its correctness
  Left-click on Run Simulation in the Flow Navigator window
  Run Behavioral Simulation
  Check the waveforms…

## Slide 25: RTL Design Complete
`timescale 1 ps / 1 ps
module half_adder_wrapper
(A,
B,
C0,
C1);
input A;
input B;
output C0;
output C1;
wire A;
wire B;
wire C0;
wire C1;
half_adder half_adder_i
(.A(A),
.B(B),
.C0(C0),
.C1(C1));
endmodule

## Slide 26: Lab 02 Part 2: Full Adder

## Slide 27: Representing Numbers with More Bits…
With 2 bits, we can represent 4 natural numbers:
    00  0
    01  1
    10  2
    11  3
With 3 bits, 8 numbers, and so on…
    000  0 100  4
    001  1 101  5
    010  2 110  6
    011  3 111  7

## Slide 28: Summing More Bits
To sum a multi-bit number, we use the same method you learned in elementary school for decimal numbers.
Example: 010 (2) + 011 (3) using 3 bits.
(3) 0 1 1 =
(2) 0 1 0 +

## Slide 29: Summing More Bits
(3) 0 1 1 =
(2) 0 1 0 +
1

## Slide 30: Summing More Bits
(3) 0 1 1 =
(2) 0 1 0 +
0 1
1

## Slide 31: Summing More Bits
(3) 0 1 1 =
(2) 0 1 0 +
0 1
1
Carry
1

## Slide 32: Summing More Bits
(3) 0 1 1 =
(2) 0 1 0 +
0 1
1

## Slide 33: Summing More Bits
(3) 0 1 1 =
(2) 0 1 0 +
1 0 1
1
The result is 5 (see slide 14), as expected!

## Slide 34: A Circuit for Addition
For every “column” of the sum:
  We actually need to sum three bits (A, B and a possible carry)
  The result can be:
    00 (0)
    01 (1)
    10 (2), i.e., 0 with a carry
    11 (3), i.e., 1 with a carry
 It requires two bits!!
(3) 0 1 1 =
(2) 0 1 0 +
1 0 1
1

## Slide 35: A 2nd Circuit for Addition
A circuit that implements “one column” of our sum is called a FULL ADDER
Let’s derive its truth table….
Earlier, we called them C0 (S) and C1 (Cout)
Input carry
(new input)

## Slide 36: Truth Table of a Full Adder
A | B | Cin | Cout | Sum
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1

## Slide 37: From the Truth Table to the Logic Gates
A | B | Cin | Sum
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1
Consider one output at a time…
Cover the ones:

## Slide 38: From the Truth Table to the Logic Gates

## Slide 39: From the Truth Table to the Logic Gates
Can we simplify it?

## Slide 40
Can we simplify it?

## Slide 41: From the Truth Table to the Logic Gates
Can we simplify it?
In practice, the EDA tool can do this for us

## Slide 42: From the Truth Table to the Logic Gates
Smaller circuit, same result…

## Slide 43: From the Truth Table to the Logic Gates
A | B | Cin | Cout
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
What about Cout
Cover the ones:

## Slide 44: From the Truth Table to the Logic Gates
Simplify…:

## Slide 45: Final Full-adder Circuit

## Slide 46: Building an Adder
To create a circuit that sums multiple bits, we simply connect multiple full adders in a chain.
Example:
0
0
1
1
0
1
0
0
1
1
0
0
1
(3) 0 1 1 =
(2) 0 1 0 +
1 0 1
1

## Slide 47: Practice Time
…again

## Slide 48: RTL Design of an Adder
Open the Vivado project for the Lab02b and create a new block design:
  IP INTEGRATOR → Create Block Design, on the left Flow Navigator bar
The “Create Block Design” window will appear:
  “Design name”: adder
“OK”
1.
2.
3.

## Slide 49: RTL Design: Input & Output Ports
Add the input and output ports:

## Slide 50: RTL Design: Logic Gates
Add the logic gates to build the full adder:

## Slide 51: RTL Design: Interconnections
Connect the different logic gates to create the circuit:
Validate the design

## Slide 52: Verify the Design (Simulation)
Simulate the design and verify its correctness

## Slide 53: RTL Design Complete
module full_adder ( input wire a, // Input a
input wire b, // Input b input wire cin, // Carry in
output wire sum, // Sum output output wire cout // Carry out
);
wire axb; // Intermediate XOR of a and b wire ab, a_xor_b_cin; // Intermediate AND gates
// XOR gate for sum
xor_gate xor1 ( .a(a), .b(b), .y(axb) );
xor_gate xor2 ( .a(axb), .b(cin), .y(sum) );
// AND gates for carry
and_gate and1 ( .a(a), .b(b), .y(ab) );
and_gate and2 ( .a(axb), .b(cin), .y(a_xor_b_cin) );
// OR gate for carry out
or_gate or1 ( .a(ab), .b(a_xor_b_cin), .y(cout));
endmodule

## Slide 54: Lab 02 Part 3: Full Adder running on the Board

## Slide 55: Implement the Circuit on the Board
Click on “Generate Bitstream” and the EDA Tool will provide the files to upload the design on the board
Open the “Hardware manager”

## Slide 56: The Hardware manager
The Hardware Manager handles the connections with the board.
To connect:
  Open target
  Auto Connect

## Slide 57: The Hardware manager
To program the device, click on Program device, then Program
Now your design is working on the board!

## Slide 58: Lab 02 Part 4: Multi-bit Adder

## Slide 59: RTL Design of a Multi-bit Adder
Open the Vivado project for the Lab02c and create a new block design:
  IP INTEGRATOR → Create Block Design, on the left Flow Navigator bar
The “Create Block Design” window will appear:
  “Design name”: adder
“OK”
1.
2.
3.

## Slide 60: RTL Design of a Multi-bit Adder
Add the logic gates to build the full adder:
Connect the different logic gates to create the circuit:
Validate the design

## Slide 61: RTL Design of a Multi-bit Adder
Your design should look like something like this:

## Slide 62: Verify the Design (Simulation)
Simulate the design and verify its correctness

## Slide 63: Authorship & License
These slides are distributed under the Creative Commons license "Attribution – Non-commercial - Share alike 2.5 Italy (CC BY-NC-SA 2.5)"
You are free to:
  to reproduce, distribute, communicate to the public, exhibit in public, represent, perform and recite this work
  to modify this work
Under the following conditions:
  Attribution - You must attribute authorship of the work to the original authors and in a way that does not suggest that they endorse you or the way you use the work.
  Non-commercial - You may not use this work for commercial purposes.
  Share Alike - If you alter or transform this work, or if you use it to create another, you may distribute the resulting work only under an identical or equivalent license to this one.
http://creativecommons.org/licenses/by-nc-sa/2.5/
Christian Conti christian.conti@polito.it
Gianvito Urgese gianvito.urgese@polito.it
Daniele Jahier Pagliari daniele.jahier@polito.it
Enrico Macii enrico.macii@polito.it
Cristiana Bolchini cristiana.bolchini@polimi.it
Fabrizio Ferrandi fabrizio.ferrandi@polimi.it
License
Authors