## Slide 1: Lab NN A Real Use Case: Neural Networks
Presented By: (Name)

## Slide 2: Boolean Algebra
Digital devices elaborate the information in their binary form (represented with 0 & 1) .
  Digital circuits or logic circuits work thanks to the information carried within the bits;
Boolean Algebra
Is used to describe the behavior of a digital circuit.
DIGITAL SIGNAL
LOGIC FUNCTION
Y = f (A, B, C, …, N)

## Slide 3: Logic Circuits
Logic circuits are used to represent an interconnected set of logic gates.
Combinational circuit:
  Made of interconnected logic gates (AND, OR, NOT, XOR, NAND, NOR), the output Y depends only on the current input.
Sequential circuit:
  Circuits made of interconnected logic gates plus an additional memory element.

## Slide 4: Components of an Electronic System

## Slide 5: What is a SoC?
A System-on-Chip (SoC) is an electronic system that includes all of its components onto a single chip:
  CPU;
  Memory;
  Peripherals;
  Interconnections;

## Slide 6: SoC Design
A System-on-Chip is composed of different units with specific tasks:
  Elaborate information;
  Store information;
  Transport information;
Each unit is designed following different methodologies to obtain the best performances when combined.

## Slide 7: SoC Design Flow
To create an SoC, industries have developed a standard design flow to speed up the engineering process:
  Front End:
    The front end includes the transformation of the SoC specification into a deployable system design
  Back End:
    Once the system functionality has been verified, the back end is in charge of creating the physical chip

## Slide 8: Electronic Design Automation Tools
EDA tools are used to design and validate the semiconductor manufacturing process;
EDA tools are used to verify that a design will meet all the project specifications;
EDA tools are used after manufacturing of the device to monitor its performance during time;

## Slide 9: Types of EDA Tools
EDAs are mostly very sophisticated and complex software programs utilized to assist during the manufacturing of an electronic system.
    Simulation tools;
    Design tools;
    Verification tools;
When high performances are required typically hardware solutions are utilized to process large amounts of data.

## Slide 10: Why EDA Tools are important?
Chips are extremely complex, containing over a billion transistors;
Managing this complexity requires the assistance of Electronic Design Automation tools;
EDA helps limit human errors in chip manufacturing and speeds up the design process;

## Slide 11: Functional Verification
Functional verification is the step related to the test in the EDA toolchain;
Ensures the correct behavior of the design and the correctness of the specifications;
Functional verification consists of stimulating the design with any possible input combination to verify the correctness of the output;

## Slide 12: Functional Verification
Functional verification is performed on any electronic design;
The challenge is creating tools to test a design quickly and efficiently without leaving anything out;
The main challenge is identifying what to test, as testing everything is not possible:

## Slide 13: Test Benches, Key Tools for Verification
A test bench is a setup used to verify the functionality of a design by simulating its operation in a controlled environment.
A test bench is used for:
  Verification, to detect and correct bugs;
  Validation, to ensure the design meets the design specifications and requirements;
  Efficiency, is always a preliminary step before hardware deployment;

## Slide 14: Test Benches, Key Tools for Verification

## Slide 15: Lab NN Neural Network: A Real Use Case

## Slide 16: Hierarchical Design: From Gates to Architectures to SoCs
+
A[15:0]
B[15:0]
Sum[15:0]
Cout
Gates
Multi-bit adder
ALU
CPU
SoC
Seen in lab02
Seen in lab03 (at high-level)

## Slide 17: SoC Applications
A System-on-a-Chip (SoC) is a computing system within a single integrated circuit.
On an SoC is possible to run software to execute complex operations.
SoC are powerful tools to accelerate and improve the performances, of a sub-set of applications.

## Slide 18: Artificial intelligence
Artificial intelligence is a field of science concerned with building computers and machines that can reason, learn, and act in such a way that would normally require human intelligence or that involves data whose scale exceeds what humans can analyze.

## Slide 19: Neural Networks
A neural network is a method in artificial intelligence (AI) that teaches computers to process data in a way inspired by the human brain.
A neural network needs thousands of operations to produce a result.

## Slide 20: The Impact of Design Choices
Design a specific system to accelerate a neural network

## Slide 21
Let’s get our hands dirty….

## Slide 22: Laboratory: An Use Case
We aim to design a small SoC capable of accelerating a neural network.
  For this laboratory, our SoC will include:
  One processing core.
  An accelerator peripheral
  A memory to store the data needed by the core, and the code of the program that it will execute
  All the components are inside the chip

## Slide 23: MINIST
Our objective is to predict handwritten digits in the fastest way possible.
We utilize the MNIST Dataset:
  The MNIST database (Modified National Institute of Standards and Technology database) is a large database of handwritten digits that is commonly used for training various image processing systems.

## Slide 24: RTL Design of an SoC
Look at the project and the design, it is made of several hierarchal components, real word applications require a lot of components and testing:
EDA tools simplify the development of these applications

## Slide 25: RTL Design of an SoC
A real application comprises different complex blocks interconnected with busses, memories, processors and peripherals.

## Slide 26: RTL Design of an SoC
Our Custom Accelerator

## Slide 27: RTL Design of an SoC
The processor

## Slide 28: Software and Hardware Stack
Take a look at the code
  There is more than one program running on the SoC:
    The Operating System
    The Server, to manage a graphical interface, and communications
    The Drivers for the accelerator

## Slide 29: Authorship & License
These slides are distributed under the Creative Commons license "Attribution – Non-commercial - Share alike 2.5 Italy (CC BY-NC-SA 2.5)"
You are free to:
  to reproduce, distribute, communicate to the public, exhibit in public, represent, perform and recite this work
  to modify this work
Under the following conditions:
  Attribution - You must attribute authorship of the work to the original authors and in a way that does not suggest that they endorse you or the way you use the work.
  Non-commercial - You may not use this work for commercial purposes.
  Share Alike - If you alter or transform this work, or if you use it to create another, you may distribute the resulting work only under an identical or equivalent license to this one.
http://creativecommons.org/licenses/by-nc-sa/2.5/
Christian Conti christian.conti@polito.it
Gianvito Urgese gianvito.urgese@polito.it
Daniele Jahier Pagliari daniele.jahier@polito.it
Enrico Macii enrico.macii@polito.it
Cristiana Bolchini cristiana.bolchini@polimi.it
Fabrizio Ferrandi fabrizio.ferrandi@polimi.it
License
Authors